## Slide 1: Modelling and Design of A 45nm SLC 3D NAND Flash CPLD
Arijit Banerjee and Sergiu Mosanu
Date: 5/15/2015

## Slide 2: End of Moore’s Law and Future Technologies
Device scaling has reached molecular dimensions
2D Moore’s law is about to end
3D can be an option to further device scaling
Courtesy: ITRS 2012

## Slide 3: 3D IC: Adding a New Dimension
Higher density
Faster clock rates
Lower in power
3D using stacked silicon die connected using through silicon via (TSV)s
2.5D using silicon interposers
2.5D using heterogeneous die packaging
Monolithic 3D ICs: 3D NAND flash
Courtesy: Yole Report 2007, and IEEE

## Slide 4: 3D FPGA
Benefits
  Higher density
  Faster clock rates
  Lower in power
  Flexibility
  Re-configurability
  Lower cost for prototyping
Combining monolithic 3D NAND flash in complex programmable logic device (CPLD) or FPGAs could drastically improve literal or logic density
Courtesy: Xilinx.com

## Slide 5: Outline
Revisiting Complex programmable logic devices (CPLD)
Modelling SLC NAND bitcell
SLC NAND planes in 3D CPLDs
3D NAND array write, read and erase operations
Circuit design for write, read and erase operations
3D configurable logic block (CLB) architecture
3D CPLD and FPGA architecture
PPA of the CLB
3D NAND array physical design and visualization

## Slide 6: Revisiting Complex Programmable Logic Devices (CPLD)
CPLDs used for gluing multiple chips to interact
Two programmable PLA planes for complex programming
The programmable planes can be replaced with two 3D NAND flash planes to achieve higher logic density

## Slide 7: Modelling an SLC NAND Bitcell in SPICE and Veriloga
SLC bitcell has two states: 1 and 0 logically
Behaviorally modelled the FNT behavior for SLC bitcell write and erase operation using a Veriloga model, a VCVS and a HVT NMOS
Veriloga model senses the gate, source and body potential of the NMOS to generate a VCVS as V(N) that exactly mimics the storage bits, write and erase operation for SLC bitcell

## Slide 8: Typical NAND Flash Array
As string is associated with a single bitline for write and read operation
The bitcells in the same page has the same wordline
Multiple pages forms a block or array which can be erased at the same time

## Slide 9: SLC NAND Planes in 3D CPLDs
Each string is of 16 SLC bitcell
Each page in two NAND planes has 16 SLC bitcell per CLB in a distributed architecture
Right figure shows a centralized 3D NAND architecture
GSL lines are controlled inside the Bot I/O, but shown individually for simplicity

## Slide 10: Ideal Write and Read Operation in SLC 3D NAND Planes

## Slide 11: Ideal Erase Operation in SLC 3D NAND Planes

## Slide 12: Actual Energy Efficient Write Read and Erase Waveforms @ 125MHz
Read
Write
Read
Erase
Read

## Slide 13: Top and Bottom I/O for Write, Read and Erase Operations for SLC 3D NANAD Array
Top and Bot I/O generate the write, read and erase voltages
They also generate write waveforms as per the data in Bot I/O

## Slide 14: Wordline Driver for Write, Read and Erase Operations for SLC 3D NANAD Array
Wordline driver generates all the necessary voltages for write, read and erase operation
Uses level converters and PMOS switches to change supply voltages

## Slide 15: 3D Configurable Logic Block Architecture for CPLD and FPGAs

## Slide 16: Distributed 3D NAND architecture for 3D CPLD and FPGAs
CLB contains the 16X8 two 3D NAND planes
Routing cost is minimal for WL and BL routability
There can be mask cost overhead for the 3D NAND planes
There can be structural brittleness in the 3D NANDs with only two planes per CLB

## Slide 17: Centralized 3D NAND architecture for 3D CPLD and FPGAs
CLB contains no 3D NAND planes: all the NAND planes are centralized in the middle of the CPLD as a cluster
Routing cost is higher for WL and BL routability and may need extra area or metal options
The mask cost overhead for the 3D NAND planes is less as it is centralized
Structurally, it is less brittle in the 3D NAND centralize array planes

## Slide 18: Input and Output Connection Boxes for 3D CPLD and FPGAs
Used flexibility of 4 overlapping connection topology for Input and output connection boxes
Muxes are PMOS-NMOS transmission gate mux for passing the true logic levels
Total of 8X4=32 programmable connection per connection box to the CLBs

## Slide 19: Switch Box Architecture for 3D CPLD and FPGAs
Switch box topology is simpler than the Planer and Wilton topology
Uses diagonal connections in the connection matrix
This topology makes the track lengths as 1 unit
Connections are made using transmission gate logic that uses distributed SRAMs to be programmed

## Slide 20: PPA of 3D CPLD or FPGAs using monolithic 3D NAND Flash Technology
Area per literal is 10X smaller using 3D NAND structures in monolithic 3D FLASH CPLDs than planer NAND CPLDs
Read, write and erase can be done up to 499MHz clock rate
Power numbers are also reasonable
Speed Max | Read Power/Literal (mW) | Write Power/Literal (mW) | Erase Power (mW)
495MHz | 51.53 | 44.65 | 66.49
 | SLC Planer NAND in CPLDs | SLC 3D NAND in CPLDs | Area Improvement
Area/Literal (μ2 / literal) | 0.48 | 0.045 | ~10X

## Slide 21: Visualization and design in 3D
Using of Autodesk Maya
Maya Embedded Language (MEL) script

## Slide 22: NAND string layer structure
Cylinder/pipe layer structure
SiNW channel
Insulator layer
Charge trapping all-around metal floating gates
Dielectric layer
Tunneling and control
All-around metal gates
Control dielectric
SiNW channel
Tunneling insulator
Charge trapping
Metal gate
Control insulator
NAND string cross-section view

## Slide 23: Bitline and wordline wiring
d=150 nm
s=150 nm
Control dielectric
SiNW channel
Tunneling insulator
Charge trapping
Metal gate
Control insulator
q
Bitline output wire
Each bitline/wordline wired to mainboard
Equal NAND string & plane spacing
Bitlines on top, at an angle
Top view

## Slide 24: Distributed 3D NAND planes in a CLB to full CPLD
8 NAND strings in a row form a NAND plane
2 NAND planes form a CLB containing 256 3D NAND FGMOS
CLB area:
NAND String area:
Area/literal:
Footprint with wires:
  literal
Configurable Logic Block (CLB)

## Slide 25: Centralized 3D NAND Buildings in a Full CPLD
CPLD consists of CLBs
Further wiring optimizations are required

## Slide 26: Conclusions
3D Flash technology in CPLD and FPGAs can provide high literal density with the support of complex Boolean functions
Programming and block erase speed is higher
Programming power consumption per literal is less than 100mW at 495MHz
Suffers from required read latching of data in the CLB even when the implementation is combinatorial

## Slide 27: References
[1] Moon, J.S.; Curtis, D.; Hu, M.; Bui, S.; Wheeler, D.; Marshall, T.; Sharifi, H.; Wong, D.; Gaskill, D.K.; Campbell, P.M.; Asbeck, P.; Jernigan, G.; Tedesco, J.; VanMil, B.; Myers-Ward, R.; Eddy, C.; Weng, X.; Robinson, J.; Fanton, M., "Self-aligned graphene-on-SiC and graphene-on-Si MOSFETs on 75 mm wafers," Device Research Conference (DRC), 2010 , vol., no., pp.209,210, 21-23 June 2010.
[2] Junho Cheon; Seongwook Choi; Young Jun Heo; Seok Ha Lee; Jaeheung Lim; Young June Park, "Fabrication of n-Type CNT Field-Effect Transistor Using Energy Band Engineering Layer Between CNT and Electrode," Electron Device Letters, IEEE , vol.34, no.11, pp.1436,1438, Nov. 2013.
[3] del Alamo, J.A., "InGaAs nanoelectronics: from THz to CMOS," Electron Devices and Solid-State Circuits (EDSSC), 2013 IEEE International Conference of , vol., no., pp.1,1, 3-5 June 2013.
[4] Mishra, A.; Pattanaik, M.; Sharma, V., "Double gate vertical tunnel FET for hybrid CMOS-TFET based low standby power logic circuits," Emerging Research Areas and 2013 International Conference on Microelectronics, Communications and Renewable Energy (AICERA/ICMiCR), 2013 Annual International Conference on , vol., no., pp.1,4, 4-6 June 2013.
[5] Zhenyu Sun; Xiuyuan Bi; Hai Li; Weng-Fai Wong; Xiaochun Zhu, "STT-RAM Cache Hierarchy With Multiretention MTJ Designs," Very Large Scale Integration (VLSI) Systems, IEEE Transactions on , vol.22, no.6, pp.1281,1293, June 2014.
[6] Kim, H.H.; Song, Y.J.; Lee, S.Y.; Joo, H.J.; Jang, N.W.; Jung, D.J.; Park, Y.S.; Park, S.O.; Lee, K.M.; Joo, S.H.; Lee, S.W.; Nam, S.D.; Kim, K., "Novel integration technologies for highly manufacturable 32 Mb FRAM," VLSI Technology, 2002. Digest of Technical Papers. 2002 Symposium on , vol., no., pp.210,211, 11-13 June 2002.
[7] Jing Xie; Yu Wang; Yuan Xie, "Yield-aware time-efficient testing and self-fixing design for TSV-based 3D ICs," Design Automation Conference (ASP-DAC), 2012 17th Asia and South Pacific , vol., no., pp.738,743, Jan. 30 2012-Feb. 2 2012.
[8] Palesko, C.; Palesko, A.; Vardaman, E.J., "Cost and yield analysis of multi-die packaging using 2.5D technology compared to fan-out wafer level packaging," Electronics System-Integration Technology Conference (ESTC), 2014 , vol., no., pp.1,5, 16-18 Sept. 2014.
[9] Qiao Chen; Suzuki, Y.; Kumar, G.; Sundaram, V.; Tummala, R.R., "Modeling, Fabrication, and Characterization of Low-Cost and High-Performance Polycrystalline Panel-Based Silicon Interposer With Through Vias and Redistribution Layers," Components, Packaging and Manufacturing Technology, IEEE Transactions on , vol.4, no.12, pp.2035,2041, Dec. 2014.
[10] Thomas, O.; Vinet, M.; Rozeau, O.; Batude, P.; Valentian, A., "Compact 6T SRAM cell with robust read/write stabilizing design in 45nm Monolithic 3D IC technology," IC Design and Technology, 2009. ICICDT '09. IEEE International Conference on , vol., no., pp.195,198, 18-20 May 2009.
[11] Panth, S.; Samadi, K.; Yang Du; Sung Kyu Lim, "High-density integration of functional modules using monolithic 3D-IC technology," Design Automation Conference (ASP-DAC), 2013 18th Asia and South Pacific , vol., no., pp.681,686, 22-25 Jan. 2013.
[12] Chang-Hong Shen; Jia-Min Shieh; Tsung-Ta Wu; Wen-Hsien Huang; Chih-Chao Yang; Chih-Jen Wan; Chein-Din Lin; Hsing-Hsiang Wang; Bo-Yuan Chen; Guo-Wei Huang; Yu-Chung Lien; Wong, S.; Chieh Wang; Yin-Chieh Lai; Chien-Fu Chen; Meng-Fan Chang; Chenming Hu; Fu-Liang Yang, "Monolithic 3D chip integrated with 500ns NVM, 3ps logic circuits and SRAM," Electron Devices Meeting (IEDM), 2013 IEEE International , vol., no., pp.9.3.1,9.3.4, 9-11 Dec. 2013.
[13] J.H. Lee et al., “Three-dimensional NAND Flash architecture design based on single-crystalline STacked ARray” in IEEE Transactions on electron devices, Vol. 59, No. 1, January 2012.
[14] B. Prince, “Vertical 3D memory technologies”, John Wiley and Sons Ltd 2014.
[15] K.T. Park, et al. “Three-dimensional 128 Gb MLC vertical NAND Flash memory with 24-WL stacked layers and 50 MB/s high-speed programming”, in IEEE journal of solid-state circuits, Vol. 50, No. 1 January 2015.
[16] Furuta, F.; Matsumura, T.; Osada, K.; Aoki, M.; Hozawa, K.; Takeda, K.; Miyamoto, N., "Scalable 3D-FPGA using wafer-to-wafer TSV interconnect of 15 Tbps/W, 3.3 Tbps/mm2," VLSI Circuits (VLSIC), 2013 Symposium on , vol., no., pp.C24,C25, 12-14 June 2013.
[17] Wolf, M.J.; Ramm, P.; Klumpp, A.; Reichl, H., "Technologies for 3D wafer level heterogeneous integration," Design, Test, Integration and Packaging of MEMS/MOEMS, 2008. MEMS/MOEMS 2008. Symposium on , vol., no., pp.123,126, 9-11 April 2008.
[18] Vaughn Betz , Jonathan Rose , Alexander Marquardt, "Architecture and CAD for Deep-Submicron FPGAs," Kluwer Academic Publishers, Norwell, MA, 1999.
[19] Soofiani, J.S.; Masoumi, N., "Area efficient switch box topologies for 3D FPGAs," New Circuits and Systems Conference (NEWCAS), 2011 IEEE 9th International , vol., no., pp.390,393, 26-29 June 2011.

## Slide 28: Questions
THANK YOU!
GO HOOS!